## Slide 1
SETP May 6, 2010
Mark Fattal
Program Quality/CM
A Configuration Management System for Prototype Programs
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 2: Agenda
History
General Requirements
CM Overview
Engineering Release Authority
Drawing Tree
Hardware Software Compatibility Matrix
Configuration Release
Prep Items
Summary
Question
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 3: History
NGC Purchased a Gulfstream II in 2006
GII Goal:
  To provide a multipurpose manned aircraft to be used as a flying test bed platform to support prototype activity, engineering concepts, program risk reduction and Headstart activity.
Independent CM Plan:
  Drafted and released in March 2007 to provide configuration of the GII Flying Test Bed (FTB) aircraft for rapid development/prototype program using the GII flight test platform.
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 4: GII Flying Test Bed
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 5: Interior Configuration Example
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 6: General Requirements
Program Quality Assigned Local Control
  On Site Flight Test Quality Engineering Performs in a dual role as Quality Engineer and Configuration Management.
Engineering Release Authority with Local Tracking Number Assigned
  Tracking number based upon current program.
Quality Maintains Originals as Aircraft Records
  Hardcopy Originals
  Electronic Archived
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 7: CM Plan Overview
Configuration Management Plan
  Defines the Process for the Control and Release Authority for
    Drawings
    Specifications
    Tests
    Instrumentation
    Special Support Equipment
    HSCM (Hardware Software Compatibility Matrix)
    Flight Release EO
All Released Documents Carry a Unique Identifier Applicable to a Specific Program (5TH Character in Drawing number)
  Example
    GII50EXXXX1: Released for an Electrical Drawing for program ABC
    GII51EXXXX2: Released for an Electrical Drawing for program XYZ
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 8: FTB Drawing Tree
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 9: CM Plan Overview
On Site Program Quality Rep is Responsible to Generate the HSCM (Hardware Software Compatibility Matrix)
The Plan Allows for Multiple Configurations/Programs Simultaneously.
Supports Either Engineering Generated Locally or Program Engineering provided for Incorporation Per Plan and Drawing Tree
The Plan Outlines the Review/Release Requirement for Every Engineering Document Type Identified in Drawing Tree.
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 10: CM Plan Approved Streamlined Approach
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 11: Takeoff
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 12: Hardware Software Compatibility Matrix
HSCM (Hardware Software Compatibility Matrix)
  Program Quality is responsible for the generating and maintaining this Matrix.
  The approved/released authorizes the applicable hardware/software configuration
  Archived Matrix’s maintain the configuration history to ensure the ability to return to a prior flight test configuration or verify the as flown condition.
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 13: Example HSCM (Notional)
LRU | Manufacture | Part No. | SW Version | FJT/Qual | Responsible Eng. | Notes
Sensor | World | 2514-A2103 | 7.1v1.10 | FJT | Tom Smith | 2/16/2010
Transponder | Waves | 500107-103 | 1.1.2a | FJT | Shirley Jones | SW 6500-118-402 v1.1.2a
Mass Storage | Store Blade | RAID | GII 103.01 | FJT | Larry Chase | dtd 2/2/10
UHF/VHF Antenna | Systems | 4511-310 | N/A | FJT | Jen Swift | 
GPS Antenna | Systems | 4545-100 | N/A | FJT | David Sandy | 
Switch Cisco | CISCO | 3750G-24TS | N/A | FJT | Mike Lumper | 
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 14: HSCM Engineering Release
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 15: HWSW - Notional Sub Tier Software
Processor | NGC | N030300G01 | NGC1234567 | GII_FLT_1.0 2/14/07 | IAW Flight Certification Report - 15-DEC 2009 | John Henry
Avionics Processor (AI) |  |  |  | 4.1.5 |  | 
Data processor (DP) |  |  |  |  |  | 
Signal Processor ISR |  |  |  |  |  | 
Signal Processor OFP |  |  |  | 1.0.1 |  | 
Output Processor (OP) |  |  |  |  |  | 
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 16: FJT/Qualification
FJT (Flight Justification Testing)
  Responsible Engineer (RE) generates FJT/Qual sheet
  Every LRU (Line Replaceable Unit)/Test Critical Component is reviewed a by the RE and approved by System Safety for operation in expected flight envelope.
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 17: FJT/Qual Sheet
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 18: Approved Program Configuration Release
Engineering Release Authority That Captures at a Top Level Modification/Configuration Changes to the A/C since last flight
  Top level project/program release.
  Signatures required dictated by plan and some optional dependent on TRR/FRR actions.
    Stress
    System Safety
Rev Letter Continues on Subsequent Release’s Thereby, Maintaining/Tacking Multiple Configuration Simultaneously.
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 19: Configuration Release Notional
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 20
IRAD -1 ASSIGNED RELEASE AUTHORITY NUMBERS |  |  |  |  |  | 
 |  |  |  | LAST UPDATE: APRIL 20, |  | 
RELEASE AUTHORITY NUMBER | DWG NUMBER | DWG REV | DRAWING TITLE | DATE RA ASSIGNED | DATE DWG RELEASED | Flt/P.I. NUMBER
RA-IRAD-001 | GII50A0001 | B | A/V INSTALLATIONS | 20-APR-10 | 21-APR-10 | 027-002/004
RA-IRAD-002 | XXXX | I/R | IRAD TRANSDUCER INSTALLATION | XXX | XXX | 027-003
RA-IRAD-003 | XXXX | I/R | FTB INSTALLATION DRAWING | XXX | XXX | N/A
RA-IRAD-004 | XXXX | N | FLIGHT TEST BED DRAWING TREE | XXX | XXX | N/A
RA-IRAD-005 | GII50F0001 | K | NGC FLIGHT CONFIGURATION RELEASE | XXX | XXX | N/A
RA-IRAD-006 | XXXX | IR | FTB INSTALLATION DRAWING | XXX | XXX | N/A
RA-IRAD-007 | XXXX | B | FAIRING MOD | XXX | XXX | 035-018
RA-IRAD-008 | XXXX | A | A/V INSTALLATIONS | XXX | XXX | N/A
RA-IRAD-009 | XXXX | IR | A/V INSTALLATIONS | XXX | XXX | N/A
RA-IRAD-010 | XXXX | A | FTB INSTALLATION DRAWING | XXX | XXX | N/A
RA-IRAD-011 | XXXX | I/R | DEMONSTRATION SYSTEM ATP | XXX | XXX | N/A
RA-IRAD-012 | XXXX | I/R | IRAD MASTER DRAWING LIST | XXX | XXX | 040-024
RA-IRAD-013 | XXXX | I/R | NGC IRAD to FTB INSTALLATION DRAWING | XXX | XXX | 040-024
RA-IRAD-014 | XXXX | S | FLIGHT TEST BED DRAWING TREE | XXX | XXX | N/A
RA-IRAD-015 | GII50F0001 | R | NGC FLIGHT CONFIGURATION RELEASE | XXX | XXX | N/A
RA-IRAD-016 | XXXX | I/R | DETAIL, RACK 5L C/B PANEL DETAIL | XXX | XXX | 052-024
RA-IRAD-017 | XXXX | I/R | XYZ ENGINE RUN GROUND ATP | XXX | XXX | 052-025
RA-IRAD-018 | GII50HWSWCM | 14 | HARDWARE SOFTWARE COMPATIBILITY MATRIX | XXX | XXX | 052-026
RA-IRAD-019 | XXXX | B | INTERCOM SYSTEM MODIFICATION | XXX | XXX | 054-003
RA-IRAD-020 | XXXX | B | FTA XYZ MASTER DRAWING LIST | XXX | XXX | N/A
RA-IRAD-021 | XXXX | A | UHF COM SYSTEM INSTALLATION | XXX | XXX | 054-003
Engineering Release Tracking Matrix (Notational)
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 21: Flight Prep Sheet used to Track Configuration Changes on Vehicle
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 22: Interior Configuration Example
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 23: Interior Configuration Example
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 24: Interior Configuration Example
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 25: Interior Configuration Example
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 26: Summary
This CM Approach Has a Proven History of Success.
  Several programs concurrently tracked on our GII.
  Other programs have adopted this methodology
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10

## Slide 27: Questions
Questions
Approved for Public Release: Northrop Grumman Aerospace Systems Case 10-0617 Dated 5/5/10